## Slide 1
Arduino PID
TargetTicksPerFrame
÷ rads_per_count
÷ 0.003173
diff_drive_controller
cmd = vel. angular
÷ loop_rate
÷ 30
rad/s
ticks/s
ticks/frame
ticks/frame
ESCRITURA (write): ros2_control -> Arduino
Constante compartida
Rads_per_count = 2π / 1980 = 0.003173 rad/ticks
Arduino encoders
readEncoder()
ticks
× rads_per_count
calcEnAngle()
Δpos / Δt
Diferencia temporal
rad (pos)
rad/s (vel)
diff_drive_controller
State_interfaces
rad, rad/s
write(): cmd / rads_per_count / loop_rate
LECTURA (read): Arduino -> ros2_control
read(): pos = enc × rads_per_count
vel = Δpos / Δt